## Slide 1: South Carolina DOT Training Workshop Geophysics Field Testing Methods, Data Reduction, and Interpretation of Results
Robert C. Bachus and Glenn J. Rix
June 5 – 26, 2020

## Slide 2
Suspension Logging

## Slide 3: Suspension Logging
Source
Triaxial
Receivers
Shear and Compression
Waves
Dz
Fluid-Filled
Borehole
Uncased is strongly preferred
OYO P-S Suspension Logger

## Slide 4: Borehole Geophysical Logging
Sonic (acoustic) logging
  e.g., Pickett, G.R. (1963). “Acoustic character logs and their applications in formation evaluation,” Journal of Petroleum Technology, 15(6), 659-667, DOI: 10.2118/452-PA
Full waveform sonic logging
  Cheng, C.H., and Toksoz, M.N., (1981). “Elastic wave propagation in a fluid-filled borehole and synthetic acoustic logs,” Geophysics 46, 1042, DOI:10.1190/1.1441242
  Paillet, F.L., and Cheng, C.H. (1991). Acoustic Waves in Boreholes, CRC Press, Boca Raton, 176 pp.
  Tang, X.-M., and Cheng, A. (2004). Quantitative Borehole Acoustic Methods, Handbook of Geophysical Exploration: Seismic Exploration, Vol. 24, Helbig, K., and Treitel, S., Eds. Elsevier, Amsterdam.
Suspension logging
  Ohya, S., Ogura, K., and Imai, T. (1984). “The suspension PS velocity logging system,” Proceedings, Offshore Technology Conference, Houston, TX, May, DOI: 10.4043/4680-MS

## Slide 5: Suspension Logging
Geophysical Service Companies
  Schlumberger
  Baker Hughes
  Robertson GeoLogging
  Reeves Wireline, Inc.
  etc.
Geotechnical Testing
  OYO Suspension Logger
    GEOVision Geophysical Services, Inc.
  Mount Sopris Instruments

## Slide 6: Suspension Logging
Monopole source
  Useful only in “fast formations” with Vs,soil > Vp,fluid because shear waves are critically refracted at the interface between the borehole fluid and surrounding formation (i.e., soil or rock)
https://www.acs.psu.edu/drussell/Demos/rad2/mdq.html

## Slide 7: Suspension Logging
Dipole source
  Useful in “slow formations” with Vs,soil < Vp,fluid because shear waves are directly generated in the formation via a bending or flexural mode of vibration of the borehole
https://www.acs.psu.edu/drussell/Demos/rad2/mdq.html
Holdorsen et al., (2006)
Note: Multiple receivers

## Slide 8: Suspension Logging
First peak
= 1823 ft/sec

## Slide 9: Suspension Logging

## Slide 10: Suspension Logging

## Slide 11: Suspension Logging
Strengths
  Ideal for deep profiling
  Requires a single borehole
  Excellent resolution; typically 1.5 to 3 ft
  Compression and shear wave measurements obtained simultaneously
  Geotechnical applications can leverage extensive development and experience for resource exploration applications
Limitations
  Proprietary nature of geotechnical applications
  Limited number of geotechnical vendors